Vehicle Kinematic

State

Vehicle state can be presented by following vehicle state vector.

x = left ( matrix {x ## y ## %psi ## v}right )

Where

x = horizontal position
y = vertical position
ψ= orientation (psi, yaw, heading)
v = speed (absolute velocity)

Control inputs can be presented by steering angle and combined value for throttle and brake. Positive throttle values are accelerating vehicle and negative values are decelerating vehicle.

u = left ( matrix {%delta ## a}right )

where

δ = steering angle
a = acceleration

Kinematic Model
When vehicle’s yaw-rate is close to zero vehicle’s position in future can be calculated by following equations
x_{t+1} = left ( matrix {x_t ## y_t ## %psi_t ## v_t}right ) + left ( matrix {v_t * cos(%psi_t) * dt ## v_t * sin(%psi_t) * dt ## v_t over Lf * %delta_t * dt ## a_t * dt}right )

where

t+1 = future state
Lf = distance from front axle to center of gravity

If vehicle’s yaw-rate is high then the above mentioned equations can’t predict vehicle state accurately.

Solution is to use CTRV state vector from unscented kalman filter project.

x = left ( matrix {x ## y ## v ## %psi ## dot %psi }right )
Problem here is that simulator doesn’t return yaw-rate. Fortunately it’s possible to calculate yaw-rate from steering angle and we can present state with (x, y, ψ, v). And then estimate state in future by following equations. We assume that acceleration is 0 and yaw-rate is 0.

dot %psi_t = v_t over Lf %delta, when %delta is small newline dot %psi_t = v_t over Lf tan(%delta), when %delta <> 0 newline newline newline x_{t+1} = left [ matrix {x_t ## y_t ## %psi_t ## v_t}right ] + left [ matrix {v_t over dot %psi_t (sin(%psi_t+dot %psi_t dt)) ## v_t over dot %psi_t (-cos(%psi_t+dot %psi_t dt)) ## dot %psi * dt ## a_t * dt}right ]

Old Stuff

Estimating vehicle XY-position when yaw-rate is zero

Estimating vehicle orientation (psi), below equation is approximation which works for small steering angles.

%psi_{ t+1 } = %psi + v_t over Lf * %delta * dt

This one is the more accurate model which gives better accuracy when steering angle is hign.

%psi_{ t+1 } = %psi + v_t over Lf * tan(%delta) * dt